Swaged RTD temperature probes  (TM1104)

Technical data：

Connecting cable:  PVC, temperature range:-5℃~+85℃

Silicone, temperature range:-50℃~+180℃

Teflon, temperature range -50℃~+260℃

Glass Fiber, temperature range:-50℃~+350℃

Protection tube:    Stainless steel 304/316, OD=4mm, 5mm,6mm

Sensor element:    Pt100 meets IEC 751

Tolerance :        Class B: △t=±(0.30 + 0.005 |t| )℃

Class A: △t=±(0.15 + 0.002 |t| )℃

Response time：t0.9  approx. 4secs, in water 0.2 m/sec, diameter 4mm

接线图 Wiring diagram 铂电阻 RTD

单支2线 1x2-wire 单支3线 1x 3-wire 双支4线 2x4-wire

单支4线 1x4-wire 双支6线 2x6-wire

白色芯线 white core wire 红色芯线 red core wire

Dimensions（外形尺寸图）

Order Details:

| TM1104 | — | (1) | — | (2) | — | 000 | — | (4) | — | (5) | — | (6) | / | (7) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

- Protection tube diameter D

4       4mm

5       5mm

6       6mm

- Insertion Length EL

100      100mm

200      200mm

500      500mm

Note：other lengths as per customers’ requitements( EL≤500mm)

- Sensor element

11       1 x Pt100 in 2-wire circuit

51       1 x Pt500 in 2-wire circuit

61       1 x Pt1000 in 2-wire circuit

13       1 x Pt100 in 3-wire circuit

14       1 x Pt100 in 4-wire circuit

12       2 x Pt100 in 4-wire circuit

16       2x Pt100 in 6-wire circuit

- Measuring range/Connecting cable

10      -5℃ ～ 85℃ /PVC

13      -50℃ ～ 180℃/Silicone

14      -50℃ ～ 260℃/Teflon

15      -50℃ ～ 350℃/Glass fiber

- Cable length L（L≥100mm）

100     100mm

200     200mm

2000    2000mm

Note：other lengths as per customers’ requitements

(100mm≤L<1000mm, L1=50mm, L≥1000mm, L1=100mm)

- Additional options

00      No

01     Strain relief spring/strain relief spring hose

02     Shielded connection cable (D≥4mm)

03      Waterproof function

07      Ferrules as per DIN 46 228 part4 (Standard)

08      Multipole connector (Providing types)

99      Special options

List the additional options in sequence, separated by commas.

# Text boxes

Applications：

The swaged RTD temperature probes are used to measure the temperature of gases or liquids, including Heaters,Ovens, Mechanical equipments and Experimental facilities etc.