Screw-in RTD temperature probes with threaded（TM1106)

Technical data:

Connecting cable:  PVC, temperature range:-5℃~+85℃

Silicone, temperature range:-50℃~+180℃

Teflon, temperature range -50℃~+260℃

Glass Fiber, temperature range:-50℃~+350℃

Protection tube:    Stainless steel 304/316, OD=4mm,5mm, 6mm,8mm

Sensor element:    Pt100, Pt500, Pt1000 meets IEC 751

Tolerance :        Class B: △t=±(0.30 + 0.005 |t| )℃

Class A: △t=±(0.15 + 0.002 |t| )℃

Response time：t0.9  approx. 4secs, in water 0.2 m/sec, diameter 4mm

接线图 Wiring diagram 铂电阻 RTD

单支2线 1x2-wire单支3线 1x 3-wire 单支4线 1x4-wire

双支4线 2x4-wire 双支6线 2x6-wire

白色芯线 white core wire 红色芯线 red core wire

Dimensions(外形尺寸图）

Order Details:

| TM1106 | — | (1) | — | (2) | — | (3) | — | (4) | — | (5) | — | (6) | / | (7) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

- Protection tube diameter D

4       4mm

5       5mm

6       6mm

8       8mm

- Protection tube Length NL

NL （100mm≤ NL≤500mm）

100     50mm≤EL<NL-50mm (NL=100)

200     50mm≤EL<NL-50mm (NL=200)

- Process connection G

119     M12×1.5

123     M16×1.5

Details in “Thread code table”

- Sensor element

11      1 x Pt100 in 2-wire circuit

51      1 x Pt500 in 2-wire circuit

61      1 x Pt1000 in 2-wire circuit

13      1 x Pt100 in 3-wire circuit

14      1 x Pt100 in 4-wire circuit

12      2 x Pt100 in 4-wire circuit

16      2 x Pt100 in 6-wire circuit

- Measuring range/Connecting cable

10    -5℃ ～ 85℃ /PVC

13    -50℃ ～ 180℃/Silicone

14    -50 ℃～ 260℃/Teflon

15    -50 ℃～ 350℃/Glass Fiber

- Cable length（L≧100）

100     100mm

200     200mm

2000    2000mm

Note：other lengths as per customers’ requirements.

(100mm≤L<1000mm, L1=50mm, L≥1000mm, L1=100mm)

- Additional options

00      No

01      Strain relief spring/strain relief spring hose

02      Shielded connecting cable (D≥4mm)

03      Waterproof function

07      Ferrules as per DIN 46 228 part4 (Standard)

08      Multipole connector (Providing types)

99      Special options

List the additional options in sequence, separated by commas.

# Text boxes

Applications：

The Screw-in RTD temperature probes with threaded are used to measure the temperature of gases or liquids, including HVAC, Refrigeration equipments, Heaters,Ovens,Plants,Mechanical equipments and Experimental facilities,etc .