Slot RTD temperature probes(TM1109)

Technical data:

Sensor element:    Pt100, Pt500, Pt1000 meets IEC 751

Tolerance :        Class B: △t=±(0.30 + 0.005 |t| )℃

Class A: △t=±(0.15 + 0.002 |t| )℃

Pressure range：2.5KV or 4KV（optional）

Operating voltage: ≤60V

Operating current：≤1mA

Connecting cable:PTFE(core),  Silicone(sheath)

Measuring range:-50℃~+180℃

接线图 Wiring diagram 铂电阻 RTD

单支2线 1x2-wire单支3线 1x 3-wire

Dimensions(外形尺寸图)

Order Details:

| TM1109 | — | (1) | — | (2) | — | (3) | — | (4) | — | (5) | — | （6） | / | （7） |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

（1）Fitting length L

50     50mm

100    100mm

（2）Width W

9   9mm

（3）Thickness d

3    3mm

（4）Sensor element

11      1 x Pt100 in 2-wire circuit

13      1 x Pt100 in 3-wire circuit

（5）Measuring range

13     -50 ℃~+180℃

（6）Cable length L（L≥100mm）

100     100mm

200     200mm

2000    2000mm

Note：other lengths as per customers’ requirements.

(100mm≤L<1000mm, L1=50mm, L≥1000mm, L1=100mm)

（7）Additional options

00      No

02      Shielded connecting cable (D≥4mm)

07      Ferrules as per DIN 46 228 part4 (Standard)

99      Special options

List the additional options in sequence, separated by commas.

# Text boxes

Applications：

The Slot RTD temperature probes are used to measure the temperature of the engine coil. It is mainly used to monitor coil temperature against damage.